# SERIAL PET/SERVER PROTOCOL

This document describes the rules for commands and data exchange between a microcontroller-based device attached to an 8-bit Commodore computer and server programs running on Windows, OS X or Linux.

## Connection Establishment Process
The device as well as the server can start the Connection Establishment Process at any time.
The requester sends a sequence of ESC EOT (0x1B, 0x04) repeated for at least 8 times, then followed by ENQ (0x05). The process is recognized at the counterpart side by receiving a sequence of at least 4 ESC EOT (0x1B, 0x04), then followed by ENQ (0x05).
If the device was requested by the server, it sends the sequence described above as requested.
If the server receives this sequence, it replies with sending ACK (0x06).
In other words:
- The server may or may not say: “please knock on my door”
- The device knocks on the servers door, either by itself or as requested
- The server says “come in”
The device then sends DC1 (0x11) if it is equipped with a IEEE-488 bus, DC2 (0x12) if it has a serial CBM bus or DC3 (0x13) if it has both.
Afterwards the device sends the version number of the protocol it speaks encoded in a byte, starting with version 0.
Further bytes sent tell the server the name of the device, encoded in ASCII and terminated with ESC EOT.
The server replies with sending either DC1 selecting the IEEE-488 bus or sending DC2 selecting the serial CBM bus for further accesses, replied with ACK (0x06) by the device.
Any mismatched reply restarts the Connection Establishment Process, where the requester should wait at least 200 ms before sending the next request.
Come that far, the device clears it's device number list to have not any device numbers, disables bus sniffing and resets all other internal variables.
Before any useful communication can occur, the device has to pull a configuration from the server first by requesting the server via CMD_SERV.
## SPSP commands
Each command or data transfer starts with a constant “CMD_” encoded in a single byte.

There is no fixed data structure for further bytes, it depends on the given command and is described in the section of each command. However, some positions have symbolic names:

Byte #	Symbolic name
0	PET_CMD
1	PET_FA, PET_LOG
2	PET_SA, PET_DR
3	PET_DATA

Some commands are followed by data bytes of any length. The end of a transmission is indicated by a sequence of ESC EOT (0x1B, 0x04). The escape character itself transmits as ESC ESC (0x1B, 0x1B).

An End-Of-File (EOF) is transmitted as ESC FS (0x1B, 0x1C). EOF terminates the transmission like ESC EOT.

Text from the Commodore is submitted as native Commodore text encoded in PETSCII. Text from the firmware, such as debug messages, is transmitted in ASCII.

On most occasions, the server replies with a one byte status code. If the status byte is not zero (DOS_00_OK), the full status message is sent after the status byte, terminated by the EOF sequence.
the error LED.

Commands (sent from device to server)

Command	#	Action
CMD_LOG	0	Sends info or debug text
CMD_OPEN	1	Opens a channel [and file]
CMD_CLOSE	2	Closes a channel [and file]
CMD_GET_BLOCK	3	Get a data block from drive/track/sector
CMD_PUT_BLOCK	4	Put a data block to drive/track/sector
CMD_READ	5	Reads from a channel
CMD_ADVANCE	6	Advances the file pointer
CMD_WRITE	7	Writes to a channel
CMD_RESET	8	Reset server
CMD_SERV	9	Ping server or pull commands from server
CMD_BUS_CMD	10	Used for bus sniffing
CMD_BUS_DATA	11	Used for bus sniffing

CMD_LOG

The server accepts text data without replying.

PET_LOG	text (ASCII)

CMD_OPEN, CMD_CMD

PET_FA: device #
PET_SA: channel #
PET_DATA: filename

The server gets a channel # (usually the SA of IEEE_488) and a filename. For the command channel #15 the filename is optional, the “filename” is parsed and executed as DOS command in such a case. CMD_CMD is an alias for CMD_OPEN, indicating that the command string did not follow a $6x OPEN command over the IEEE bus but was written directly into the command channel #15. This separation is only needed for bus sniffing.

The file type and access mode is appended to the filename following Commodore DOS syntax. E.g.:

FILENAME,S,W	: open sequential file for writing
$0:*	: open directory listing for reading
1:FILENAME,L,(LEN)	: open relative file with record length LEN

The server parses the filename and tries to open the file. He replies with a Commodore DOS code, DOS_00_OK for success or an error code otherwise. Some examples for possible error conditions are:

DOS_20_READ_ERROR
DOS_22_READ_ERROR
DOS_25_WRITE_ERROR
DOS_30_SYNTAX_ERROR
DOS_62_FILE_NOT_FOUND
DOS_63_FILE_EXISTS
DOS_64_FILE_TYPE_MISMATCH
DOS_70_NO_CHANNEL
DOS_72_DISK_FULL

Appears in bus log as:

OPN #FA (in case of CMD_OPEN)
DTA #FA (in case of CMD_CMD)
<data>

CMD_CLOSE

PET_FA: device #
PET_SA: channel #

The channel is closed. Following activities are triggered depending on the channel association:

Read files: nothing
Write files: write EOF marker, update directory entry
Command channel (#15): nothing
Direct access buffer: Flush buffer, free buffer

The reply is either DOS_00_OK or an error code.

Appears in bus log as:

CLO #SA

CMD_GET_BLOCK

PET_FA:	device #
PET_DR: drive #
PET_TR: track #
PET_SE: sector #

The server reads a 256 byte block of binary data from the specified position (drive / track / sector) and transmits this sector in raw binary format (no ESC sequences). The status byte follows immediately after the last (256 th.) data byte.

Some possible status codes are:

DOS_00_OK
DOS_66_ILLEGAL_TRACK_OR_SECTOR
DOS_74_DRIVE_NOT_READY

Does not affect the bus log.

CMD_PUT_BLOCK

PET_FA:	device #
PET_DR: drive #
PET_TR: track #
PET_SE: sector #

The server receives and writes a 256 byte block of binary data to the specified position (drive / track / sector). The data are transmitted in raw binary format (no ESC sequences). The status byte is sent in response.

Some possible status codes are:

DOS_00_OK
DOS_26_WRITE_PROTECT
DOS_66_ILLEGAL_TRACK_OR_SECTOR
DOS_74_DRIVE_NOT_READY

Does not affect the bus log.

CMD_READ

PET_FA:	device #
PET_SA:	channel #
PET_DATA:	# of bytes to read (0..255)

Before transmitting any bytes, the server internally saves the current position of the corresponding file pointer and restores the position after the read process. The file pointer is advanced only by the CMD_ADVANCE command sent by the firmware.

The reply are the requested number of data bytes or fewer if EOF occurred followed by either DOS_00_OK or an error code.

Some possible return codes are:

DOS_00_OK
DOS_02_EOF	(read to end-of-file)
DOS_20_READ_ERROR
DOS_22_READ_ERROR
DOS_70_NO_CHANNEL

Does not affect the bus log.

CMD_ADVANCE

PET_FA:	device #
PET_SA:	channel #
PET_DATA:	unsigned offset

Advance the file pointer by the designated number of bytes.

Appears in bus log as:

DTA #SA
<data>

CMD_WRITE

PET_FA:	device #
PET_SA:	channel #
PET_DATA:	binary stream

The server replies with a return code. Some examples for possible return codes are:

DOS_00_OK
DOS_25_WRITE_ERROR
DOS_72_DISK_FULL

Appears in bus log as:

DTA #SA
<data>

CMD_SERV

The server replies either with ACK (0x06) or NAK (0x15) to confirm the established connection. If the device does not receive any of those replies within 1000 ms, it sends CMD_RESET and returns to stand-alone mode.

NAK confirms an established connection and no further action is required.

ACK confirms the established connection and forces the device to pull CONF-commands (described later) from the server.

CMD_RESET

The server flushes and frees all buffers. All open files are closed. Appears in bus log as:

--- BUS RESET ---

CMD_BUS_CMD

PET_FA: IEEE command

Used for logging only. Indicates that the given byte was transferred with ATN low. Values not listed below should appear as
UKN followed by the value in hexadecimal notation.

0x20 – 0x3E:	LISTEN # (0..30)
0x3F:	UNLISTEN
0x40 – 0x5E:	TALK # (0..30)
0x5F:	UNTALK
0x6x:	DATA # (0..15)
0xEx:	CLOSE # (0..15)
0xFx:	OPEN # (0..15)

CMD_BUS_DATA

PET_LOG: <data>

Used for logging only. Used to transmit bus traffic by third party devices.

## CONF commands
These commands are sent from the server to the device only when requested by the device by sending a CMD_SERV command, which it should do regularly. Once requested, the server can send as many CONF-commands as he wishes. Sending CONF_DONE ends the transmission and further CONF-commands can only get send when requested by the device with CMD_SERV again.

CONF_DONE	Ends the transmission of CONF-commands
CONF_ADD_DEVICE_NUMBER	Gives the device a (further) device address
CONF_RM_DEVICE_NUMBER	Removes a device address
CONF_SNIFF	Enables or disables bus sniffing

CONF_DONE
Tells the device that the server has no more CONF-commands to send.
CONF_ADD_DEVICE_NUMBER
#address
The server sends the address encoded in a single byte it would like to react the device upon and the device replies by either sending ACK (0x06) or NAK (0x15) if its maximum number of device numbers is already reached.

CONF_RM_DEVICE_NUMBER
#address
The server sends the address encoded in a single byte the device should ignore from now on. The device always replies with ACK (0x06) regardless if it did react on that address in the past or not.

CONF_SNIFF
boolean on/off
The server sends a byte to switch bus sniffing on or off. Any value greater than zero enables bus sniffing.
## DOS COMMAND SUMMARY

The server parser recognizes and executes these Commodore DOS commands:

Short	Long	BASIC 4	Description
C	COPY	COPY / CONCAT	Copy or concatenate files
D	DUPLICATE	BACKUP	Copy disk
I	INITIALIZE		Intialize disk (read BAM)
N	NEW	HEADER	Format disk
P	POSITION	RECORD	Seek record #
R	RENAME	RENAME	Rename file
S	SCRATCH	SCRATCH	Delete files
V	VALIDATE	COLLECT	Reconstruct BAM
/			Create or change to subdirectory

Direct access commands:

Short	Alternative	Description
U1	UA	Read disk block to buffer
U2	UB	Write buffer to disk block
B-A	BLOCK-ALLOCATE	Allocate block in BAM
B-F	BLOCK-FREE	Free block in BAM
B-R	BLOCK-READ	Read partial block to buffer
B-W	BLOCK-WRITE	Write partial buffer to disk
M-R		Read drive RAM/ROM
M-W		Write to drive RAM

Non Commodore commands:

Short	Description
CD	Change directory
MD	Make directory
RD	Remove directory
T	Copy ISO 8601 time and date string into status